Based on the technical sources, here is a consolidated reference guide for the ATMega328P USART0 module, organized by registers and operational flow.
### 1. USART0 Register Reference
All primary USART registers are located in the Extended I/O memory region.
Register	Address	Primary Function
UDR0	0xC6	I/O Data Register: Buffer for data being sent (TXB) or received (RXB).
UCSR0A	0xC0	Control & Status A: Contains status flags (RXC, TXC, UDRE) and error flags (FE, DOR, UPE).
UCSR0B	0xC1	Control & Status B: Enables/disables Receiver (RXEN) and Transmitter (TXEN), and manages interrupts.
UCSR0C	0xC2	Control & Status C: Sets communication mode (Sync/Async), Parity, Stop bits, and Character size.
UBRR0L	0xC4	Baud Rate Low: Lower 8 bits of the 12-bit baud rate generator.
UBRR0H	0xC5	Baud Rate High: Upper 4 bits of the 12-bit baud rate generator.
PRR	0x64	Power Reduction: Bit 1 (PRUSART0) must be written to 0 to provide power to the USART module.

### 2. Operational Flow Steps
#### Step 1: Initialization
This must be performed before any communication occurs.
1. Calculate the Baud Rate: Determine the 12-bit value needed for UBRR based on your system clock and desired speed.
2. Set the Baud Rate: Write the high byte to UBRR0H and the low byte to UBRR0L.
3. Configure Frame Format: Set the mode, parity, stop bits, and character size (bits per frame) in UCSR0C.
4. Enable Hardware: Set the TXEN0 and RXEN0 bits in UCSR0B to activate the transmitter and receiver.
#### Step 2: Sending Data (Transmitting)
1. Check Status: Poll the UDRE0 (Data Register Empty) flag in UCSR0A. Wait until it becomes 1.
2. Load Data: Write the character to be sent into the UDR0 register.
3. (Optional) Verify Completion: If you need to know when the physical shift out is finished (e.g., to turn off an RS-485 driver), poll the TXC0 flag.
#### Step 3: Receiving Data
1. Check Status: Poll the RXC0 (Receive Complete) flag in UCSR0A. It becomes 1 when a character is ready.
2. Check for Errors: Read UCSR0A bits FE0 (Frame Error), DOR0 (Data Overrun), and UPE0 (Parity Error) before reading the data.
3. Read Data: Retrieve the character from the UDR0 register.

### 3. Key Hardware Constraints
- Order of Reading: You must read the status flags in UCSR0A before you read the data from UDR0. Reading UDR0 changes the state of the internal receive buffer (FIFO) and clears the error flags for that character.
- 9-Bit Logic: If using 9-bit data frames, the 9th bit in UCSR0B must be written (for TX) or read (for RX) before the low 8 bits in UDR0 are accessed.
- Extended Instructions: Because these registers are at addresses above 0x5F, you must use LDS/STS (Load/Store Direct) instructions rather than IN/OUT if programming in Assembly.